## Slide 1: Veterinary Radiology
Safety and Procedures

## Slide 2: What is a radiograph?
When an xray beam (a form of electromagnetic radiation) penetrates tissue to form a picture

## Slide 3: Our Goal….
Safety for animals and personnel
Less radiation because of preparation and training
Diagnostic films the first time

## Slide 4: Safety First
Lead: blocks xray beams
  Aprons
  Glasses
  Thyroid shields
  Gloves
    Placed ON HANDS- not laying over hands

## Slide 5: Safety First
Dosimeter
  Measures radiation exposure
  Should be worn by anyone with increased risk of occupational exposure

## Slide 6: Hardware…
Cassettes: hold the film and have an intensifying screen built in, different for different views
Xray machine: needs to be warmed up
Caliper: measures patient for correct settings
Processor: develops radiographs
Labeler: labels radiographs before developed

## Slide 7: Hardware
Intensifying Screens:
  Smooth, shiny, white inner layer of the film cassette that improves radiographic detail
  The screen allow for a lower mAs setting, which decreases the chance of blurriness due to movement, decreases patient radiation exposure, and prolongs the life of the x-ray tube
  Cleaning: at least once a month. Use the manufacturer recommended product. If unavailable, use 70% alcohol

## Slide 8: Radiology Terminology
Radiopaque
  Appearing white to light gray in color
  May indicate hard tissue or that exposure was too low
Radiolucent
  Appearing black to dark gray
  May indicate soft tissue or that exposure was too high

## Slide 9: Mechanisms of Xrays…
Xrays pass completely through some things and therefore the film is black
   air, gas
  Other things absorb the xrays creating an image that is variances of white
  Metal, bone appear white
  Everything else is gray-shades in between
      Soft tissue
      Organs
      Tumors/masses
      Food material in digestive tract

## Slide 10: 3 Factors That Produce a Radiograph
kVP= kilovoltage peak
- the energy (power) or strength of the beam
mA= milliamperage
- quantity of xray beams used
S= seconds
- exposure time: shorter time will reduce blurriness

## Slide 11: Radiology Logs
Legally required document
Comparison on techniques for patient follow-up films
Recording quality of film taken
State practice acts outline required information for the log

## Slide 12: Technique Chart
List of settings on the machine based upon thickness of area to be exposed
Grid technique
  Film not in contact with patient
  Radiation source is lower
Tabletop technique
  Cassette is in contact with patient

## Slide 13: Film Identification
Hospital name, address, and phone number
Veterinarian’s name
X-ray number
Client’s name
Patient’s name
Date
Directional label

## Slide 14: Stretch and Reflect
What is kVp?
What is a technique chart?
What material is our PPE made of?

## Slide 15: Standard VS. Digital Radiography

## Slide 16: Developing Film
Manual
  Done by hand
  Takes longer
  Is less expensive
Automatic
  Done by machine
  More expensive
  Quicker
  Better quality

## Slide 17: Manual and Automatic
Developing tanks
  Developer solution
    Left side
    Develops the film
  Fixer solution
    Right side
    Fixes film and maintains life of film
  Wash tank
    Far right
    Rids film of chemicals

## Slide 18: Digital Processing
Image is transferred to a computer
Image is read on a computer screen
Image quality tends to be better

## Slide 19: Radiation Sickness
Radiation will cause:
  Birth defects
  Aplastic anemia (damage to bone marrow and stem cells)
  Degenerative changes in the extremities (necrosis)
  Cancer

## Slide 20: NEVER----
Assist or take a radiograph if you are not wearing protective gear or do not have a badge
Put your hands or other body parts in
a radiograph beam
Forget to prepare before getting your
animal on the table
Leave animal on table alone
Be near radiation if you are pregnant
or nursing

## Slide 21: Never…Never….NEVER
Let a client help with taking a radiograph!!!